## Slide 1: State machines keys
James Barker
Kiefer Capps

## Slide 2: Overview
State Machines
Keys

## Slide 3: State Machines
Similar to switch case
Can transition between defined states
Dependant on output
Five Types:
  Function
  If/Else
  Switch
  Mealy
  Hierarchical

## Slide 4: SM: Functions
No global variable
Each state is a separate function

## Slide 5: SM: If/Else
If/else statements
  Route path to new “state”
Need a “state” variable

## Slide 6: SM: Switch
Each case is a state
Entire case statement has to be looped
Allows compiler to find best path

## Slide 7: SM: Mealy (Finite)
Depend on two factors
  Current state of machine
  Triggering source

## Slide 8: SM: Hierarchical
“Nested”
State machine within a state machine

## Slide 9: Keys
Using switches to trigger an event in the software
Must consider:
  Pull Up/ Pull Down Resistors
        External Resistors
        Internal Resistors
  Proper Synchronization
        Real time/Gadfly Synchronization
        Interrupt Synchronization

## Slide 10: Keys: Pull Up/Down Resistors
No pull up/down = floating values
Floating values cause false triggers in the switch
By adding a resistor to ground or VCC we can always keep a defined state of HIGH or LOW, preventing false triggers

## Slide 11: Internal vs External Resistors
External pull up/down resistors can be used to simplify programming.
Internal pull up/down resistors can lower cost, simplifies circuitry, and is convenient when parts are not readily available.

## Slide 12: Gadfly Synchronization
The program continually “asks” the status of the switch, also called polling
Even when the switch is not pressed the program is checking the status

## Slide 13: Interrupt Synchronization
The program runs other functions until the switch is pressed.
When the switch is pressed, it interrupts the program and runs it’s function.
Only certain pins can be interrupts. Lecture 5 shows detailed steps how to work around this.

## Slide 14: Lab Questions
Q: Do you need to use internal pull-ups for the keys on the joystick shield?
A: No, looking at the schematic external resistor are attached so an internal pull-up is not require.
Q:How would your code look like for switches which are connected to pull-down resistors instead of pull-up resistors?
A: PTAD = 0xFF; /// write 1‘s to prevent false interrupts
to set as pull-down instead of pull-up
PTAD = 0x00; /// write 0‘s to prevent false interrupts

## Slide 15: Lab Questions: Continued
Q: What fundamental steps are required on the FRDM board to use the reset button as user button? What is the advantage of this? What is the disadvantage of this?
A: To turn the reset button to a user button the switch has to be reconfigured, eliminating the reset feature.
Advantage: A built in button allows more features to be added
Disadvantage: Must disconnect and reconnect power to restart